## Slide 1
WEBINAR
Raspberry Pi Headless Setup
Setting up your raspberry pi without a Monitor and Keyboard & Mouse

## Slide 2
Requirements
WEBINAR
Raspberry Pi
Power Adaptor
Sd Card
Laptop (Windows, Mac or Linux)
Raspberry Pi Imager Installed
Phone with Fing app installed (or any other network scan app)
Good Internet Connection

## Slide 3
Step 1: Download and install Raspberry Pi Imager
WEBINAR
Download it at : https://www.raspberrypi.org/software/

## Slide 4
Step 2: Launch and Configure the OS
WEBINAR
Press : Cntrl + Shift + X to open hidden configurations

## Slide 5
Step 3: Format and Install the OS
WEBINAR

## Slide 6
Step 4: Plug in the SD card and Power ON
WEBINAR

## Slide 7
Step 5: Find the IP address of The pi with Fing
WEBINAR
On a mac : arp –a
*fing not required

## Slide 8
Step 6: SSH into the Pi from PowerShell
WEBINAR
Command : ssh hostname@ip Ex: ssh pi@192.168.0.128

## Slide 9
Step 7: Update the OS
WEBINAR
Command : sudo apt-get update
Command : sudo apt-get upgrade

## Slide 10
Step 8: Enable VNC
WEBINAR
Command : sudo raspi-config

## Slide 11
Step 9: Download VNC Viewer on the Laptop
WEBINAR

## Slide 12
Step 10: Connect to the Raspberry Pi
WEBINAR

## Slide 13
Step 10: Connect to the Raspberry Pi
WEBINAR

## Slide 14
Step 11: Connect to the Raspberry Pi
WEBINAR

## Slide 15
Thank you
WEBINAR
for coming!
-YoungWonks Team